## Slide 1: Chapter 1
1.1 Introduction to digital signals and systems, Properties and
operations on digital signals, Introduction to biosignals:
ECG, EEG, EMG, PPG
1.2 Classification of signals, system, LTI system
1.3 Convolution in time domain (linear & circular),
Correlation.

## Slide 2: Signal
A signal is a pattern of variation that carry information.
Signals are represented mathematically as a function of one or more independent variable.
A picture is brightness as a function of two spatial variables, x and y.
In this course signals involving a single independent variable, generally refer to as a time, t are considered. Although it may not represent time in specific application.
A signal is a real-valued or scalar-valued function of an independent variable t.

## Slide 3: Example of signals
Electrical signals like voltages, current and EM field in circuit
Acoustic signals like audio or speech signals (analog or digital)
Video signals like intensity variation in an image
Biological signal like sequence of bases in gene
Noise which will be treated as unwanted signal

## Slide 4: Classification of Signal
Continuous Time and Discrete Time Signals
A signal is said to be continuous when it is defined for all instants of time.
A signal is said to be discrete when it is defined at only discrete instants of time

## Slide 5: Signal Processing
Representation, transformation and manipulation of signals and the information they contain.
Signal operation include:
(1) Transform, filter, inspection, spectrum analysis;
(2) Modulation and coding;
(3) Analog Signal Processing;
(4) Digital Signal Processing.

## Slide 6: Processing of analog signal with digital methods
(1) Digitalized process for analog signals
Sample
Quantizer
Coder
xa(t)
x(n)
(2) Digital processing method
A/D
DSP
D/A
xa(t)
ya(t)
Filter
x(n)
y(n)
Filter

## Slide 7: Features of Digital System
(1) High accuracy: Floating point-8,16,32,64 bits
(2) High reliability: VLSI (analog: drift, calibration)
(3) Flexible: DSP, Software, FPGA, VHDL
(4) Easy to integrate
(5) Deal with high dimensional signals
(6) Low costs: reusable, reconfigurable
(7) Data logging
(8) Adaptive capability

## Slide 8: Discrete Signal and Discrete Time Signal

## Slide 9: Digital Signal

## Slide 10: Digital Signal

## Slide 11: Representation of Discrete Time Signals
Functional Representation

## Slide 12: Representation of Discrete Time Signals
Graphical Representation

## Slide 13: Representation of Discrete Time Signals
Tabular Representation

## Slide 14: Representation of Discrete Time Signals
Sequence Representation

## Slide 15: Standard Discrete Time Signal

## Slide 16: Standard Discrete Time Signal

## Slide 17: Standard Discrete Time Signal

## Slide 19: Standard Discrete Time Signal

## Slide 22: Sampling theorem
A continuous time signal can be represented in its samples and can be recovered back when sampling frequency fs is greater than or equal to the twice the highest frequency component of message signal (fm).

## Slide 23: Relationship between analog and digital signal by sampling

## Slide 24: Classification of Discrete Time Signals

## Slide 25: Deterministic and Non-deterministic Signals
A signal is said to be deterministic if there is no uncertainty with respect to its value at any instant of time. Or, signals which can be defined exactly by a mathematical formula (Eg: Ramp , Unit Step, exponential, sinusoidal) are known as deterministic signals.

## Slide 26: Deterministic and Non-deterministic Signals
A signal is said to be non-deterministic if there is uncertainty with respect to its value at some instant of time. Non-deterministic signals are random in nature hence they are called random signals. Random signals cannot be described by a mathematical equation. They are modelled in probabilistic terms.

## Slide 27: Periodic and Aperiodic Signals

## Slide 35: Symmetric(EVEN) and antisymmetric(ODD) signals

## Slide 36: Symmetric(EVEN) and antisymmetric(ODD) signals

## Slide 37: Symmetric(EVEN) and antisymmetric(ODD) signals

## Slide 38: Symmetric(EVEN) and antisymmetric(ODD) signals

## Slide 39: Symmetric(EVEN) and antisymmetric(ODD) signals

## Slide 40: Symmetric(EVEN) and antisymmetric(ODD) signals

## Slide 41: Energy and Power Signals

## Slide 42: Energy and power signals

## Slide 46: Causal, Noncausal, Anticausal Signals
Causal Signal
Non Causal if defined for n<=0 or for both n>0 and n<=0
If system is non causal then:
A non-causal signal can be converted into causal by multiplying it by unit step signal.
When a non causal signal is defined for only n<0 then it is called anticausal signal.

## Slide 48: Mathematical operations on Discrete Time Signals

## Slide 49: 1. Scaling

## Slide 50: 1. Scaling

## Slide 52: 2. Folding

## Slide 53: 3.Time Shifting of Discrete Time Signals
X(n) signal will be shifted by variable m i.e. x(n)=x(n-m)
m is positive integer signal is delayed by m units of time.
Delay results in shifting each sample of x(n) to right.
m is negative integer signal is advanced by m units of time.
Advance results in shifting each sample of x(n) to left.

## Slide 55: 4. Addition of Discrete Time Signal

## Slide 57: 5.Multiplication of Discrete time signals

## Slide 59: Discrete Time System
Discrete time system is device or algorithm which accepts input in discrete signal form to produce output or response in discrete time signal form.

## Slide 60: Discrete Time System

## Slide 61: LTI (Linear Time Invariant) System
A discrete time system is linear if it obeys principle of superposition and time invariant if input output relationship does not change with time.
When system satisfies property of linearity and time invariance it is called as LTI system.

## Slide 62: Block Diagram and Signal Flow graph Representation of DT System
Basic elements of Representation are:
Adder
Constant Multiplier – Constant scaling factor
Unit Delay Element – one sample unit to delay
Unit Advance Element - one sample unit to advance

## Slide 64: Block Diagram and Signal Flow graph Representation of DT System

## Slide 67: Static system and Dynamic System
Static System – Output depends on only current input samples but not on past or future samples – no memory
Dynamic System – Opposite of static

## Slide 70: Time Invariant and Time Variant System
A system is said to be time invariant if its input output characteristics do not change with time.

## Slide 72
Test the following system for time variance

## Slide 73
Test the following system for time variance

## Slide 74
Test the following system for time variance

## Slide 75
Test the following system for time variance

## Slide 76: Linear and Non Linear System

## Slide 77: Linear and Non Linear System(Check for Linearity)

## Slide 78
Test the following system for linearity.

## Slide 85: Causal and Non Causal Systems

## Slide 86: Causal and Non Causal Systems

## Slide 87: Causal and Non Causal Systems

## Slide 88: Causal and Non Causal Systems

## Slide 89: Stable and Unstable

## Slide 90: Stable and Unstable

## Slide 92: FIR and IIR Systems
FIR system (Finite duration Impulse Response System) , the impulse response consists of finite number of samples.
IIR system (Infinite duration Impulse Response System) , the impulse response consists of infinite number of samples.

## Slide 94: Discrete or Linear Convolution

## Slide 95: Discrete or Linear Convolution
In linear convolution the x1 and x2 sequences are non periodic , hence convolution result x3 is also non periodic.
Linear convolution is said to be aperiodic.

## Slide 96: Procedure

## Slide 97: Properties

## Slide 101: Graphical Method

## Slide 114: Circular Convolution

## Slide 115: Circular Convolution-Procedure

## Slide 134: Correlation
Used when two signals are to be compared.
Measure of degree to which two signals are similar.
Cross Correlation – correlation of two separate signals
Auto Correlation – correlation of signal with itself.

## Slide 135: Cross Correlation

## Slide 136: Cross Correlation
Number of Samples = N1+N2-1
Start of Sequence mi = n1-(n2+N2-1)
End of Sequence mf = mi+(N1+N2-2)

## Slide 137: Auto Correlation

## Slide 138: Auto Correlation
Number of Samples = 2N-1
Start of Sequence
initial value of m:mi = -(N-1)
End of Sequence
  final value of m: mf = mi+(2N-2)

## Slide 149
Thank you