## Slide 1: Introduction to Biosignals
ECG, EMG, EEG, PPG
Biomedical Signal Fundamentals

## Slide 2: Biosignals – Definition
• Signals generated by physiological activities
• Electrical or optical in nature
Electrical signals measure voltage generated by ion movement in tissues.
Optical signals measure changes in light due to blood flow in tissues.
• Reflect organ and system functions

## Slide 3: Why Biosignals Matter
• Disease diagnosis
• Continuous monitoring
• Wearable & remote healthcare
• Research and AI-based analysis

## Slide 4: Classification of Biosignals
• Electrical: ECG, EMG, EEG
• Optical: PPG
• Mechanical
• Chemical
• Thermal

## Slide 5: ECG – Electrocardiogram
• Electrical activity of the heart
• P–QRS–T waveform
• Amplitude: ~1 mV
• Frequency: 0.05–150 Hz

## Slide 6: ECG – Applications
• Heart rate & rhythm analysis
• Arrhythmia detection
• Cardiac stress testing

## Slide 7: EMG – Electromyogram
• Electrical activity of skeletal muscles
• Generated during contraction
• Amplitude: µV–mV
• Frequency: 20–500 Hz

## Slide 8: EMG – Applications
• Neuromuscular disorder diagnosis
• Prosthetic & robotic control
• Sports biomechanics

## Slide 9: EEG – Electroencephalogram
• Electrical activity of the brain
• Measured from scalp electrodes
• Amplitude: µV
• Frequency: 0.5–100 Hz

## Slide 10: EEG – Brain Waves
• Delta (0.5–4 Hz)
• Theta (4–8 Hz)
• Alpha (8–13 Hz)
• Beta (13–30 Hz)
• Gamma (>30 Hz)

## Slide 11: EEG – Applications
• Epilepsy detection
• Sleep analysis
• Brain–computer interface

## Slide 12: PPG – Photoplethysmogram
• Optical measurement of blood volume changes
• Uses LED & photodetector
• Non-invasive
• Used in wearables

## Slide 13: PPG – Applications
• Heart rate monitoring
• Oxygen saturation (SpO₂)
• Fitness trackers & smartwatches

## Slide 14: Comparison of ECG, EMG, EEG, PPG
ECG: Heart (Electrical)
EMG: Muscle (Electrical)
EEG: Brain (Electrical)
PPG: Blood flow (Optical)

## Slide 15: Signal Challenges
• Noise & motion artifacts
• Low amplitude signals
• Baseline drift
• Need for filtering

## Slide 16: Conclusion
• Biosignals reveal vital physiological information
• ECG, EMG, EEG, PPG are core signals
• Foundation of biomedical instrumentation