## Slide 1: Chapter 3
Image Transform: Frequency Domain Representation and Enhancement

## Slide 2: Syllabus
Image Transform: Frequency Domain Representation and Enhancement (10-CO3)
3.1 Introduction , DFT and its properties, radix-2 algorithm(2- DFT ), FFT algorithm: divide and conquer approach, Dissemination in Time(DIT)-FFT
3.2 Discrete Cosine Transform, Walsh Transform, Hadamard Transform, Haar Transform, Principal component Analysis(PCA/Hoteling Transform), Introduction to Wavelet Transform
3.3 Low Pass and High Pass Frequency domain filters: Ideal, Butterworth, Homomorphic filter
Self-Learning Topic: Discrete Sine Transform (DST)

## Slide 3: Image Transforms
Extensively used in image processing and image analysis.
Transform is basically a mathematical tool, which allows us to move from one domain to another domain (time domain to the frequency domain).
Transforms change the representation of a signal by projecting it onto a set of basis functions.
The transforms do not change the information content present in the signal.

## Slide 4: NEED FOR TRANSFORM
(i) Mathematical Convenience:
Every action in time domain will have an impact in the frequency domain.
The complex convolution operation in time domain is equal to simple multiplication operation in the frequency domain
(ii) To Extract more Information:
Transforms allow us to extract more relevant information.

## Slide 5: Classification of Image Transforms

## Slide 6: Image Transform
1) Orthogonal sinusoidal basis function
One of the most powerful transforms with orthogonal sinusoidal basis function is the Fourier transform.
The transform which is widely used in the field of image compression is discrete cosine transform.

## Slide 7: Image Transform
2) Non-sinusoidal orthogonal basis function
The transforms whose basis functions are non-sinusoidal in nature.
One of the important advantages of wavelet transform is that signals (images) can be represented in different resolutions.

## Slide 8: Image Transform
3) Basis function depending on statistics of input signal
The transform whose basis function depends on the statistics of input signal are KL transform and singular value decomposition.
The KL transform is considered to be the best among all linear transforms with respect to energy compaction.

## Slide 9: Image Transform
4) Directional transformation
The transforms whose basis functions are effective in representing the directional information of a signal include Hough transform, Radon transform, Ridgelet transform and Contourlet transform.

## Slide 10: FOURIER TRANSFORM
Fourier transform is widely used in the field of image processing.
A Fourier transform is used to transform an intensity image into the domain of spatial frequency.
A continuous time signal x(t) is converted into discrete time signal x(nT ) by sampling process, where T is the sampling interval

## Slide 11
A continuous time signal x(t) is converted into discrete time signal x(nT ) by sampling process, where T is the sampling interval
Where X(ejω ) is known as Discrete-Time Fourier Transform (DTFT) and is a continuous function of ω. The relation between ω and Ω is given by
ω = ΩT
ω =2πf ×T
where T is the sampling interval and is equal to 1/ fs . Replacing T by 1/ fs in above equation we get
ω = k × 2π
To limit the infinite number of values to a finite number, above equation is modified as ω/2π= k/N

## Slide 12: Discrete Fourier Transform

## Slide 13: Discrete Fourier Transform

## Slide 14: Discrete Fourier Transform
Discrete Fourier transform for a finite sequence is given by:
Evaluating summation for finite sequence for 0 to N-1.
k/N corresponds to frequency F
N corresponds to time for discrete signals

## Slide 15: Inverse Discrete Fourier Transform

## Slide 16: Unitary transform
Unitary Transform= A discrete linear transform is unitary if its transform matrix conforms to the unitary condition
A × AH = I
where A = transformation matrix,
AH represents Hermitian matrix.
AH= A*T
I = identity matrix
When the transform matrix A is unitary, the defined transform is called unitary transform

## Slide 17: Orthogonal DFT
If A is unitary and has only real elements , then it is orthogonal matrix
A is orthogonal if A.A’ = I

## Slide 18: Image Transform
1) Check whether the DFT matrix is unitary or not.

## Slide 23: Unitary Transform
unitary transformation preserves the signal energy
Most unitary transforms pack a large fraction of the energy of the image into relatively few of the transform coefficients.
Few of the transform coefficients have significant values and these are the coefficients that are close to the origin

## Slide 24: Properties of DFT-
Periodicity

## Slide 25: Properties of DFT
Linearity

## Slide 26: Properties of DFT
Circular Convolution

## Slide 27: Properties of DFT
Time reversal
If the sequence is circularly folded , its DFT is also circularly folded.

## Slide 28: Properties of DFT
Time shift

## Slide 29: Properties of DFT
Conjugation
DFT of complex conjugate of any sequence is equal to complex conjugate of DFT of that sequence , with sequence delayed by k samples in frequency domain.
DFT{x(n)}=X(k)
DFT{X*(n)}=X*(N-k)

## Slide 30: 2D DISCRETE FOURIER TRANSFORM

## Slide 31
where R(k, l ) represents the real part of the spectrum and I(k, l) represents the imaginary part

## Slide 32: Twiddle factor

## Slide 33: Twiddle factor

## Slide 34: Twiddle Factor

## Slide 35: DFT:
For N of length 4,range of n, k = [0 1 2 3] each.
Hence X(n) = x(0)WNn.0+x(1)WNn.1+x(2)WNn.2 + x(3)WNn.3
 |  | x(0) | x(1) | x(2) | x(3)
X(0) | = | W40x0 | W40x1 | W40x2 | W40x3
X(1) | = | W41x0 | W41x1 | W41x2 | W41x3
X(2) | = | W42x0 | W42x1 | W42x2 | W42x3
X(3) | = | W43x0 | W43x1 | W43x2 | W43x3

## Slide 36
 |  | x(0) | x(1) | x(2) | x(3)
X(0) | = | W40x0 | W40x1 | W40x2 | W40x3
X(1) | = | W41x0 | W41x1 | W41x2 | W41x3
X(2) | = | W42x0 | W42x1 | W42x2 | W42x3
X(3) | = | W43x0 | W43x1 | W43x2 | W43x3
 |  | x(0) | x(1) | x(2) | x(3)
X(0) | = | W40 | W40 | W40 | W40
X(1) | = | W40 | W41 | W42 | W43
X(2) | = | W40 | W42 | W44 | W46
X(3) | = | W40 | W43 | W46 | W49
Can be rewritten as:

## Slide 37: Cyclic property of twiddle factors
The "cyclic property" of twiddle factors means that their values repeat periodically, meaning that the sequence of twiddle factors for a given FFT size will repeat after a certain number of cycles, which is equal to the size of the DFT (N) itself; essentially, the values "wrap around" and start repeating again, allowing for efficient computation in FFT algorithms by reusing calculated values.

## Slide 38
Compute the DFT of the four-point sequence x(n)={0,1,2,3}

## Slide 39
The effective determinant of above is 1/4.
Conversion in system matrices of DFT and IDFT obtained by replacing by j by –j.
Inversion of above matrix is:

## Slide 40: Cyclic property of twiddle factors
For an 8-point DFT

## Slide 41: FOR 8 point DFT: N=8
The system Matrix is:
W80x0 | W80x1 | W80x2 | W80x3 | W80x4 | W80x5 | W80x6 | W80x7
W81x0 | W81x1 | W81x2 | W81x3 | W81x4 | W81x5 | W81x6 | W81x7
W82x0 | W82x1 | W82x2 | W82x3 | W82x4 | W82x5 | W82x6 | W82x7
W83x0 | W83x1 | W83x2 | W83x3 | W83x4 | W83x5 | W83x6 | W83x7
W84x0 | W84x1 | W84x2 | W84x3 | W84x4 | W84x5 | W84x6 | W84x7
W85x0 | W85x1 | W85x2 | W85x3 | W85x4 | W85x5 | W85x6 | W85x7
W86x0 | W86x1 | W86x2 | W86x3 | W86x4 | W86x5 | W86x6 | W86x7
W87x0 | W87x1 | W87x2 | W87x0 | W87x4 | W87x5 | W87x6 | W87x7

## Slide 42: The characteristic matrix of 8-point DFT is:

## Slide 43: DFT and its Inverse Conversion in system matrices of DFT and IDFT obtained by replacing by j by –j..
DFT
IDFT
Effective
determinant

## Slide 44: DFT of Image Matrix (2D)

## Slide 45: DFT of Image Matrix (2D)

## Slide 49: Fast Fourier Transform
FFT is method of computing DFT with reduced number of calculations.
Computational efficiency is achieved if we adopt a divide and conquer approach.
Approach is based on decomposition of N point DFT into successively smaller DFTs.

## Slide 50: FFT-Divide & Conquer
Size 8 DFT
Size 4 DFT
Size 4 DFT
Size 2 DFT
Size 2 DFT
Size 2 DFT
Size 2 DFT
p = 2 (radix 2)

## Slide 51: Radix-2 FFT
Radix-x: here ‘x’ represents number of samples in each group made at the first stage. They are generally equal.
N=2^m
m is number of stages
N point sequence is decimated into 2 point sequences, further from the results of 2 point DFTs, the 4 point DFTs can be computed and so on.

## Slide 52: Radix -2
Radix-2 is the first FFT algorithm. It was proposed by Cooley and Tukey in 1965.
The algorithms appear either in
(a) Decimation In Time (DIT),
(b) Decimation In Frequency (DIF).
DIT and DIF, both yield same complexity and results. They are complementary.
We shall stress on 8 to radix 2 DIT FFT

## Slide 53: No. of Calculations in DFT

## Slide 54
Size 8DFT
Size 4 DFT
Size 2 DFT
Size 2 DFT
Size 4 DFT
Size 2 DFT
Size 2 DFT

## Slide 56: DIT- FFT Flowgraphs
The Radix-2 Decimation in Time (DIT) Fast Fourier Transform (FFT) is an efficient algorithm to compute the Discrete Fourier Transform (DFT). It reduces the computational complexity from O(N²) (in direct DFT computation) to O(N log₂N).
Steps to compute the DFT using Radix-2 DIT FFT:
Step 1: Check for Radix-2 Condition
Ensure that the number of input points, N, is a power of 2 (N = 2^m).
If N is not a power of 2, pad the sequence with zeros until it becomes a power of 2.

## Slide 57: DIT- FFT Flowgraphs
Step 2: Bit-Reversal Permutation
Rearrange the input sequence x(n) into bit-reversed order.
The index positions of the input sequence are converted into their binary equivalents, then reversed, and finally mapped to the new sequence.
Step 3: Perform FFT Computation Using Butterfly Operations
The algorithm follows a divide-and-conquer approach by recursively breaking down the DFT into smaller computations.
The number of stages in the FFT is log₂N.
Each stage consists of multiple butterfly computations, where a butterfly operation processes two inputs to produce two outputs.

## Slide 58
Step 4: Iterate for All Stages
Repeat the butterfly computations for log₂N stages.
The number of groups (or sub-DFTs) doubles at each stage, while the number of points per group halves.
Step 5: Output the Final FFT Coefficients
After completing log₂N stages, the transformed sequence X(k) represents the DFT of the input sequence x(n).

## Slide 59
radix-2 DIT butterfly operation.
radix-4 DIT butterfly operation.

## Slide 60
(a) Signal flow graph of 8-point radix-2 DIT FFT (b) radix-2 DIT butterfly operation.

## Slide 61
Refer example 5.5, page 5.38 of digital signal processing, Nagoorkani

## Slide 62: DIT-FFT
Steps to find DFT using Radix 2 DIT FFT:

## Slide 63
Ex: Draw the signal flow graph of the 4-point FFT, then use to it to find the spectrum of the sequence x(n)={1,-1,2,3}.
The even numbered samples are x(0) and x(2)
The odd numbered samples are x(1) and x(3)
X(0)=G(0)+W40 H(0)
X(1)=G(1)+W41 H(1)
X(2)=G(0)+W42 H(0)
X(3)=G(3)+W43 H(3)
And again G(3)=G(1)and H(3)=H(1), then:
X(3)=G(1)+W43 H(1)
E=

## Slide 67: Discrete Cosine Transform (DCT)
The discrete cosine transforms are the members of a family of real-valued discrete sinusoidal unitary transforms.
A discrete cosine transform consists of a set of basis vectors that are sampled cosine functions.
DCT is a technique for converting a signal into elementary frequency components and it is widely used in image compression.

## Slide 75: IDCT

## Slide 76: Symmetric and Asymmetric
Transformation Matrix – T
Image Matrix – f
If Transformation matrix is symmetric:
F = TfT
If Transformation matrix is asymmetric:
F = TfT’

## Slide 77: Hadamard Transform

## Slide 79: Hadamard Transform
Hadamard of Sequence
X[n]={H(N).x(n)}
Inverse Hadamard of Sequence
x[n] = 1/N{H(N).X(n)}
Hadamard of image (2D)
Hadamard is symmetric transform
F = TfT

## Slide 81: Walsh Transform

## Slide 82: Haar Transform

## Slide 83: Haar Transform

## Slide 84: IMAGE ENHANCEMENT IN THE FREQUENCY DOMAIN
If we multiply each element of the Fourier coefficient by a suitably chosen weighting function then we can accentuate certain frequency components and attenuate others.
This selective enhancement or suppression of frequency components is termed Fourier filtering or frequency domain filtering.
The spatial representation of image data describes the adjacency relationship between the pixels.
On the other hand, the frequency domain representation clusters the image data according to their frequency distribution.
In frequency domain filtering, the image data is dissected into various spectral bands, where each band depicts a specific range of details within the image.
The process of selective frequency inclusion or exclusion is termed frequency domain filtering.
It is possible to perform filtering in the frequency domain by specifying the frequencies that should be kept and the frequencies that should be discarded.

## Slide 85: IMAGE ENHANCEMENT IN THE FREQUENCY DOMAIN
f(m,n) – original image
F(k,l) – FT of original image
h(m,n) – Filtering mask
H(k,l) – FT of filtering mask

## Slide 86
1. Low pass filter:
1. Low pass filter removes the high frequency components that means it keeps low frequency components. It is used for smoothing the image. It is used to smoothen the image by attenuating high frequency components and preserving low frequency components.
Mechanism of low pass filtering in frequency domain is given by:
G(u, v) = H(u, v) . F(u, v)
where F(u, v) is the Fourier Transform of original image
and H(u, v) is the Fourier Transform of filtering mask

## Slide 87
1. Low pass filter:
2. High pass filter: High pass filter removes the low frequency components that means it keeps high frequency components. It is used for sharpening the image. It is used to sharpen the image by attenuating low frequency components and preserving high frequency components.
Mechanism of high pass filtering in frequency domain is given by:
H(u, v) = 1 - H'(u, v)
where H(u, v) is the Fourier Transform of high pass filtering
and H'(u, v) is the Fourier Transform of low pass filtering

## Slide 88
1. Low pass filter:
3. Band pass filter: Band pass filter removes the very low frequency and very high frequency components that means it keeps the moderate range band of frequencies. Band pass filtering is used to enhance edges while reducing the noise at the same time.
Band pass filter removes the very low frequency and very high frequency components that means it keeps the moderate range band of frequencies. Band pass filtering is used to enhance edges while reducing the noise at the same time.

## Slide 89: Low Pass (LP) Filters
Ideal low-pass filter (ILPF)
Butterworth low-pass filter (BLPF)
Gaussian low-pass filter (GLPF)

## Slide 90: Ideal Low-pass (LP) filtering
Preserves low frequencies, attenuates high frequencies.
  Cut off all high-frequency components of the Fourier transform that are at a distance greater than a specified distance D0 (cut off frequency) from the origin of the (centered) transform
  The transfer function (frequency domain filter) is defined by
  D(u,v) is the distance from point (u,v) to the origin (center) of the frequency domain filter
  Usually, the image to be filtered is even-sized, in this case, the center of the filter is (M/2,N/2). Then the distance D(u,v) can be obtained by

## Slide 91: Ideal Low-pass (LP) filtering
How to determine the cutoff frequency D0?
  One way to do this is to compute circles that enclose specified amounts of total image power PT.

## Slide 92: How does D0 control smoothing? (cont’d)
D0 controls the amount of blurring
r=8 (90%)
r=78 (99%)

## Slide 93: Ringing Effect
Sharp cutoff frequencies produce an overshoot of image features whose frequency is close to the cutoff frequencies (ringing effect).
h=f*g

## Slide 94
Ringing effect is clear in most cases except for the last one.
Ringing effect is the consequence of applying ideal lowpass filters
Ringing effect is clear in most cases except for the last one.
Ringing effect is the consequence of applying ideal lowpass filters

## Slide 95: Butterworth Lowpass Filters
A butterworth lowpass filter (BLPF) of order n with cutoff frequency at a distance D0 from the origin is given by the following transfer function
  BLPF does not have a sharp discontinuity
  For BLPF, the cutoff frequency is defined as the frequency at which the transfer function has value which is half of the maximum

## Slide 96: Examples of Application of BLPF
Same order but with different cutoff frequencies
  The larger the cutoff frequency, the more details are reserved

## Slide 97: Butterworth LPF

## Slide 98: Butterworth LP filter (BLPF)
In practice, we use filters that attenuate high frequencies smoothly (e.g., Butterworth LP filter)  less ringing effect
n=1
n=4
n=16

## Slide 99: Spatial Representation of BLPFs
n=1 n=2 n=5 n=20

## Slide 100: Comparison: Ideal LP and BLPF
ILPF
BLPF
D0=10, 30,
60, 160,
460
n=2
D0=10, 30,
60, 160,
460

## Slide 101: Gaussian Lowpass Filters
GLPF is given by the following (centered ) transfer function
  (u0,v0) is the center of the transfer function
  It is [M/2, N/2] if M,N are even and [(M+1)/2,(N+1)/2] if M,N are odd numbers
  Dose GLPF suffer from the ringing effect?

## Slide 102
Example: smoothing by GLPF (1)

## Slide 103
Examples of smoothing by GLPF (2)
D0=100
D0=80

## Slide 104: High-Pass filtering
A high-pass filter can be obtained from a low-pass filter using:
= 1 -
D0

## Slide 105: High-pass filtering (cont’d)
Preserves high frequencies, attenuates low frequencies.

## Slide 106: Butterworth high pass filter (BHPF)
In practice, we use filters that attenuate low frequencies smoothly (e.g., Butterworth HP filter)  less ringing effect

## Slide 107: Comparison: IHPF and BHPF
IHPF
BHPF
D0=30,60,160
n=2
D0=30,60,160

## Slide 108: Gaussian HP filter
GHPF
BHPF

## Slide 109: Comparison: BHPF and GHPF
GHPF
BHPF
D0=30,60,160
n=2
D0=30,60,160

## Slide 110: Homomorphic filtering
Many times, we want to remove shading effects from an image (i.e., due to uneven illumination)
  Enhance high frequencies
  Attenuate low frequencies but preserve fine detail.

## Slide 111: Homomorphic Filtering (cont’d)
Consider the following model of image formation:
In general, the illumination component i(x,y) varies slowly and affects low frequencies mostly.
In general, the reflection component r(x,y) varies faster and affects high frequencies mostly.
i(x,y): illumination
r(x,y): reflection
IDEA: separate low frequencies due to i(x,y)
from high frequencies due to r(x,y)

## Slide 112: How are frequencies mixed together?
When applying filtering, it is difficult to handle
low/high frequencies separately.
Low and high frequencies from i(x,y) and r(x,y)
are mixed together.

## Slide 113: Can we separate them?
Idea:
Take the ln( ) of

## Slide 114: Steps of Homomorphic Filtering
(1) Take
(2) Apply FT:
or
(3) Apply H(u,v)

## Slide 115: Steps of Homomorphic Filtering (cont’d)
(4) Take Inverse FT:
or
(5) Take exp( ) or

## Slide 116: Example using high-frequency emphasis
Attenuate the contribution made by illumination and amplify the contribution made by reflectance
Attenuate the contribution made by illumination and amplify the contribution made by reflectance

## Slide 117: Homomorphic Filtering: Example

## Slide 118: Homomorphic Filtering: Example

## Slide 119: PCA Steps:
Centre the data by subtracting off the mean
Choose the direction with largest variation, place an axis in that direction
Look at the remaining variations, find another axis that is that is orthogonal to the first axis and covers maximum variations

## Slide 120: Standard deviation
Standard deviation, is simply the square root of the average square distance of data points to the mean. In the equation below, the numerator contains the sum of the differences between each datapoint and the mean, and the denominator is simply the number of data points (minus one), producing the average distance.

## Slide 121: Variance
Variance is simply standard deviation squared, and is often expressed as s^2
For both variance and standard deviation, squaring the differences between data points and the mean makes them positive, so that values above and below the mean don’t cancel each other out.

## Slide 122: Covariance
Variance and Covariance are a measure of the “spread” of a set of points around their center of mass (mean)
• Variance – measure of the deviation from the mean for points in one dimension e.g. heights
• Covariance as a measure of how much each of the dimensions vary from the mean with respect to each other.
• Covariance is measured between 2 dimensions to see if there is a relationship between the 2 dimensions e.g. number of hours studied & marks obtained.
• The covariance between one dimension and itself is the variance

## Slide 123: Covariance
So, if you had a 3-dimensional data set (x,y,z), then you could measure the covariance between the x and y dimensions, the y and z dimensions, and the x and z dimensions.
Measuring the covariance between x and x , or y and y , or z and z would give you the variance of the x , y and z dimensions respectively.

## Slide 124: Covariance Matrix
Representing Covariance between dimensions as a matrix e.g. for 3 dimensions:
• Diagonal is the variances of x, y and z
• cov(x,y) = cov(y,x) hence matrix is symmetrical about the diagonal
• N-dimensional data will result in NxN covariance matrix

## Slide 125: Covariance
Exact value is not as important as it’s sign.
(+) A positive value of covariance indicates both dimensions increase or decrease together e.g. as the number of hours studied increases, the marks in that subject increase.
(-) A negative value indicates while one increases the other decreases, or vice-versa e.g. time spent on social media vs performance in exam.
(zero) If covariance is zero: the two dimensions are independent of each other e.g. heights of students vs the marks obtained in a subject

## Slide 126: Covariance
Why bother with calculating covariance when we could just plot the 2 values to see their relationship?
Ans:
Covariance calculations are used to find relationships between dimensions in high dimensional data sets (usually greater than 3) where visualization is difficult.

## Slide 127: Eigen vectors
The resulting vector is not integer multiple of the original vector
The resulting vector is exactly 4 times the original vector. This is called eigenvector.
We can transform and change matrices into new vectors by multiplying a matrix with a vector. The multiplication of the matrix by a vector computes a new vector. This is the transformed vector.

## Slide 128: Eigenvector
If the new transformed vector is just a scaled form of the original vector then the original vector is known to be an eigenvector of the original matrix
An eigenvector is a vector that does not change when a transformation is applied to it, except that it becomes a scaled version of the original vector.
Eigenvalue— The scalar that is used to transform (stretch) an Eigenvector.

## Slide 129: Eigenvector and Eigenvalue
An eigenvector does not change direction in a transformation:
In this shear mapping the red arrow changes direction, but the blue arrow does not. The blue arrow is an eigenvector of this shear mapping because it does not change direction, and since its length is unchanged, its eigenvalue is 1.
1 means no change,
2 means doubling in length,
−1 means pointing backwards along the eigenvalue's direction

## Slide 130: The Mathematics
For a square matrix A, an Eigenvector and Eigenvalue make this equation true:

## Slide 131: How do we find these eigen things?
We start by finding the eigenvalue:
we know this equation must be true: Av = λv
Now let us put in an identity matrix so we are dealing with matrix-vs-matrix:
Av = λIv
Bring all to left hand side:
Av − λIv = 0
If v is non-zero then we can solve for λ using just the determinant:
| A − λI | = 0
Let's try that equation on our previous example:

## Slide 134: PCA
Principal components analysis (PCA) is a technique that can be used to simplify a dataset
• It is a linear transformation that chooses a new coordinate system for the data set such that greatest variance by any projection of the data set comes to lie on the first axis (then called the first principal component),the second greatest variance on the second axis, and so on.
• PCA can be used for reducing dimensionality by eliminating the later principal components.

## Slide 135: Steps Involved in the PCA
Step 1: Standardize the dataset.
Step 2: Calculate the covariance matrix for the features in the dataset.
Step 3: Calculate the eigenvalues and eigenvectors for the covariance matrix.
Step 4: Sort eigenvalues and their corresponding eigenvectors.
Step 5: Pick k eigenvalues and form a matrix of eigenvectors.
Step 6: Transform the original matrix.

## Slide 136: Example
1. Standardize the Dataset
Assume we have the below dataset which has 4 features and a total of 5 training examples.

## Slide 137: Example
First, we need to standardize the dataset and for that, we need to calculate the mean and standard deviation for each feature.
After applying the formula for each feature in the dataset is transformed as below:

## Slide 138: Example
2. Calculate the covariance matrix for the whole dataset
The formula to calculate the covariance matrix:
Since we have standardized the dataset, so the mean for each feature is 0 and the standard deviation is 1.

## Slide 139: Example
var(f1) = ((-1.0-0)² + (0.33-0)² + (-1.0-0)² +(0.33–0)² +(1.33–0)²)/5 var (f1) = 0.8
cov(f1,f2) =((-1.0–0)*(-0.632456-0) + (0.33–0)*(1.264911-0) + (-1.0–0)* (0.632456-0)+ (0.33–0)*(0.000000 -0)+ (1.33–0)*(-1.264911–0))/5 cov(f1,f2) = -0.25298

## Slide 140: Example
In the similar way be can calculate the other covariances and which will result in the below covariance matrix

## Slide 141: Example
3. Calculate eigenvalues and eigen vectors.
Aν-λIν =0 ;
(A-λI)ν = 0
Since we already know ν is a non- zero vector, only way this equation can be equal to zero, if
det(A-λI) = 0

## Slide 142: Example
Solving the above equation |M|= 0
λ = 2.51579324 , 1.0652885 , 0.39388704 , 0.02503121

## Slide 143: Example
Eigenvectors:
Solving the (A-λI)ν = 0 equation for ν vector with different λ values:
For λ = 2.51579324, solving the above equation using Cramer's rule, the values for v vector are
v1 = 0.16195986 v2 = -0.52404813 v3 = -0.58589647 v4 = -0.59654663

## Slide 144: Example
Going by the same approach, we can calculate the eigen vectors for the other eigen values. We can from a matrix using the eigen vectors.
4. Sort eigenvalues and their corresponding eigenvectors.
Since eigenvalues are already sorted in this case so no need to sort them again.

## Slide 145: Example
5. Pick k eigenvalues and form a matrix of eigenvectors
If we choose the top 2 eigenvectors, the matrix will look like this:
6. Transform the original matrix.
Feature matrix * top k eigenvectors = Transformed Data

## Slide 147: Wavelet Transform
https://medium.com/@koushikc2000/2d-discrete-wavelet-transformation-and-its-applications-in-digital-image-processing-using-matlab-1f5c68672de3